## Slide 1: X86 Assembly
Mooly Sagiv
http://www.egr.unlv.edu/~ed/assembly64.pdf
https://godbolt.org/
‪https://www.cis.upenn.edu/~stevez/ CS341

## Slide 2: Compiler Phases
Program
text
Parser
AST
Syntax errors
Semantic
Analysis
Annotated
AST
Semantic errors
IR
Optimizer
IR
Code
Generation
assembly
Code Generation

## Slide 3: Outline
X86 history
Memory hierarchy
Stack frames
Compiling a simple example
Running a simple example

## Slide 4: Intel’s X86 Architecture

## Slide 5: X86 history
Year | Invention
1978 | Intel introduces 8086
1982 | 80186, 80286
1985 | 80386
1989 | 80486 (100MHz, 1μm)
1993 | Pentium
1995 | Pentium Pro
1997 | Pentium II/III
2003 | Pentium M(Banias), Intel Core
2006 | Intel Core 2
2008 | Intel Core i3/i5/i7
2011 | SandyBridge / IvyBridge
2013 | Haswell
2014 | Broadwell
2015 | Skylake (core i3/i5/i7/i9) (2.4GHz, 14nm)
2016 | Xeon Phi

## Slide 7: Memory vs. CPU Speed

## Slide 8: Solutions
Architecture & Compiler
  Machine registers utilized by compiler
Explore locality

## Slide 9: Memory Hierarchy
Registers
Cache
1.Smaller
2. Faster
3. More expensive
RAM
Secondary Storage
(disk drive, SSID)
Tertiary Storage
(Remote storage, optical)

## Slide 10: Stack Frames
Allocate a separate space for every procedure incarnation
Relative addresses
Provide a simple mean to achieve modularity
Supports separate code generation of procedures
Naturally supports recursion
Efficient memory allocation policy
  Low overhead
  Hardware support may be available
LIFO policy
Not a pure stack
  Non local references
  Updated using arithmetic

## Slide 12: A Typical Stack Frame
higher addresses
previous frame
current frame
lexical pointer
argument 1
argument 2
dynamic link
return address
temporaries
argument 2
argument 1
outgoing parameters
lower addresses
next frame
frame size
frame pointer
stack pointer
outgoing parameters
registers
locals
administrative

## Slide 13: Pascal 80386 Frame
lexical pointer
higher addresses
previous frame
current frame
lexical pointer
argument 2
argument 1
locals
return address
temporaries
argument 1
argument 2
outgoing parameters
saved registers
lower addresses
next frame
rbp
rsp
previous ebp

## Slide 14: Compiling a simple example
#include <stdio.h>
main() {
printf("factorial(2)=%d", factorial(2));
}
.LC0:
.string "factorial(2)=%d"
main:
push rbp
mov rbp, rsp
mov edi, 2
call factorial(int)
mov esi, eax
mov edi, OFFSET FLAT:.LC0
mov eax, 0
call printf
mov eax, 0
pop rbp
ret

## Slide 15: Compiling factorial
int factorial(int num) {
if (num == 1) return 1 ;
else return num * factorial(num -1 );
}
. factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret

## Slide 16
factorial(int):
…
.LC0:
.string "factorial(2)=%d"
main:
push rbp
mov rbp, rsp
mov edi,2
call factorial(int)
mov esi, eax
mov edi, OFFSET FLAT:.LC0
mov eax, 0
call printf
mov eax, 0
pop rbp
ret
Code/Data
Stack
rbp
rsp
777777777

## Slide 17
factorial(int):
…
.LC0:
.string "factorial(2)=%d"
main:
push rbp
mov rbp, rsp
mov edi, 2
call factorial(int)
mov esi, eax
mov edi, OFFSET FLAT:.LC0
mov eax, 0
call printf
mov eax, 0
pop rbp
ret
Code/Data
Stack
rbp
rsp
777777777
777777777

## Slide 18
factorial(int):
…
.LC0:
.string "factorial(2)=%d"
main:
push rbp
mov rbp, rsp
mov edi, 2
call factorial(int)
mov esi, eax
mov edi, OFFSET FLAT:.LC0
mov eax, 0
call printf
mov eax, 0
pop rbp
ret
Code/Data
Stack
rbp
rsp
777777777
777777777

## Slide 19
factorial(int):
…
.LC0:
.string "factorial(2)=%d"
main:
push rbp
mov rbp, rsp
mov edi, 2
call factorial(int)
L4: mov esi, eax
mov edi, OFFSET FLAT:.LC0
mov eax, 0
call printf
mov eax, 0
pop rbp
ret
Code/Data
Stack
rbp
rsp
777777777
777777777
2
edi

## Slide 20
factorial(int):
…
.LC0:
.string "factorial(2)=%d"
main:
push rbp
mov rbp, rsp
mov edi, 2
call factorial(int)
L2: mov esi, eax
mov edi, OFFSET FLAT:.LC0
mov eax, 0
call printf
mov eax, 0
pop rbp
ret
Code/Data
Stack
rbp
rsp
777777777
777777777
2
edi

## Slide 21
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
2
edi
L4

## Slide 22
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
2
edi
L4
777777777

## Slide 23
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
2
edi
L4
777777777
777777756

## Slide 24
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
2
edi
L4
777777777
777777756
777777740

## Slide 25
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
2
edi
L4
777777777
777777756
777777740
2

## Slide 26
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
2
edi
L4
777777777
777777756
777777740
2
cr
NE

## Slide 27
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
2
edi
L4
777777777
777777756
777777740
2

## Slide 28
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
2
edi
L4
777777777
777777756
777777740
2
2
eax

## Slide 29
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
2
edi
L4
777777777
777777756
777777740
2
1
eax

## Slide 30
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
1
edi
L4
777777777
777777756
777777740
2
1
eax

## Slide 31
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
L5: imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
1
edi
L4
777777777
777777756
777777740
2
1
eax
L5

## Slide 32
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
L5: imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
1
edi
L4
777777777
777777756
777777740
2
1
eax
L5
777777756

## Slide 33
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
L5: imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
2
edi
L4
777777777
777777756
777777740
2
2
eax
L5
777777756
777777736
777777732

## Slide 34
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
L5: imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
1
edi
L4
777777777
777777756
777777740
2
1
eax
L5
777777756
777777736
777777732
777777716
1

## Slide 35
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
L5: imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
1
edi
L4
777777777
777777756
777777740
2
1
eax
L5
777777756
777777736
777777732
777777716
1
cr
E

## Slide 36
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
L5: imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
1
edi
L4
777777777
777777756
777777740
2
1
eax
L5
777777756
777777736
777777732
777777716
1

## Slide 37
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
L5: imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
1
edi
L4
777777777
777777756
777777740
2
1
eax
L5
777777756
777777736
777777732
777777716
1

## Slide 38
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
L5: imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
1
edi
L4
777777777
777777756
777777740
2
1
eax
L5
777777756
777777736
777777732
777777716
1

## Slide 39
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
L5: imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
1
edi
L4
777777777
777777756
777777740
2
1
eax
L5
777777756
777777736
777777732
777777716
1

## Slide 40
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
L5: imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
1
edi
L4
777777777
777777756
777777740
2
1
eax
L5
777777756
777777736
777777732
777777716
1

## Slide 41
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
L5: imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
1
edi
L4
777777777
777777756
777777740
2
1
eax
777777756
777777736
777777732
777777716
1

## Slide 42
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
L5: imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
1
edi
L4
777777777
777777756
777777740
2
2
eax
777777756
777777736
777777732
777777716
1

## Slide 43
factorial(int):
push rbp
mov rbp, rsp
sub rsp, 16
mov DWORD PTR [rbp-4], edi
cmp DWORD PTR [rbp-4], 1
jne .L2
mov eax, 1
jmp .L3
.L2:
mov eax, DWORD PTR [rbp-4]
sub eax, 1
mov edi, eax
call factorial(int)
L5: imul eax, DWORD PTR [rbp-4]
.L3:
leave
ret
…
Code/Data
Stack
rbp
rsp
777777777
777777777
1
edi
L4
777777777
777777756
777777740
2
2
eax
777777756
777777736
777777732
777777716
1

## Slide 44
factorial(int):
…
.LC0:
.string "factorial(3)=%d"
main:
push rbp
mov rbp, rsp
mov edi, 3
call factorial(int)
L4: mov esi, eax
mov edi, OFFSET FLAT:.LC0
mov eax, 0
call printf
mov eax, 0
pop rbp
ret
Code/Data
Stack
rbp
rsp
777777777
777777777
1
edi
777777777
777777756
777777740
2
2
eax
777777756
777777736
777777732
777777716
1

## Slide 45
factorial(int):
…
.LC0:
.string "factorial(2)=%d"
main:
push rbp
mov rbp, rsp
mov edi, 2
call factorial(int)
L4: mov esi, eax
mov edi, OFFSET FLAT:.LC0
mov eax, 0
call printf
mov eax, 0
pop rbp
ret
Code/Data
Stack
rbp
rsp
777777777
777777777
1
edi
777777777
777777756
777777740
2
2
eax
777777756
777777736
777777732
777777716
1
2
esi

## Slide 46
factorial(int):
…
.LC0:
.string "factorial(3)=%d"
main:
push rbp
mov rbp, rsp
mov edi, 3
call factorial(int)
L4: mov esi, eax
mov edi, OFFSET FLAT:.LC0
mov eax, 0
call printf
mov eax, 0
pop rbp
ret
Code/Data
Stack
rbp
rsp
777777777
777777777
LC0
edi
777777777
777777756
777777740
2
2
eax
777777756
777777736
777777732
777777716
1
2
esi

## Slide 47
factorial(int):
…
.LC0:
.string "factorial(3)=%d"
main:
push rbp
mov rbp, rsp
mov edi, 3
call factorial(int)
L4: mov esi, eax
mov edi, OFFSET FLAT:.LC0
mov eax, 0
call printf
mov eax, 0
pop rbp
ret
Code/Data
Stack
rbp
rsp
777777777
777777777
LC0
edi
777777777
777777756
777777740
2
0
eax
777777756
777777736
777777732
777777716
1
2
esi

## Slide 48: Summary
Pentium X86 is a powerful CISC architecture
Stack frames provide memory locality
  Simple allocation/deallocation
  Efficient even for recursive calls
  Architecture support may help
Understanding compiler generated code is not easy